## Slide 1: Introduction to Boolean Logic
TEJ2O

## Slide 2: Remember that…
1 in the Binary System represents
  ON or YES
0 in the Binary System represents
  OFF or NO
Boolean logic is a part of almost every aspect of COMPUTER ELETRONICS

## Slide 3: What is Boolean Logic
In the 1850s George Boole developed a new form of algebra, now called Boolean algebra in his honour.
Boolean equations use the binary number system to provide a very precise way of illustrating the logic of computer chips.
Interesting fact: Boolean equations were used long before computers or even electricity was invented!
- Details from Computer Engineering: An Activities-based approach by Smyth and Stephenson

## Slide 4: Examining Logic Gates
A gate is where data (or electricity) flows through. The gate takes the input (usually A and/or B) and gives an output (Y)

## Slide 5: Summary of the Gates
Schematic | Gate | Symbol | Boolean Equation
 | AND |  | Y = A  B
 | OR | + | Y = A + B
 | NOT | - | Y = Ā
 | NOR | - + | Y = A + B
 | XOR | + | Y = A + B
 | NAND | -  | Y = A  B

## Slide 6: TRUTH TABLES
Understanding the logic behind the gates will help us determine the output
We use truth tables to determine the outputs based on different inputs.

## Slide 7: AND
A | B | Y (Output)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Both inputs must be 1(YES) to get a 1(YES) as output.
Y = A  B

## Slide 8: OR
A | B | Y (Output)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
If either input is 1 (YES) the output is 1 (YES).
Y = A + B

## Slide 9: NOT
A | Y (Output)
0 | 1
1 | 0
Output is opposite of input.
Y = A

## Slide 10: NOR
A | B | Y (Output)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
RESULT IS OPPOSITE OF OR
Y = A + B

## Slide 11: XOR
A | B | Y (Output)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Only one input can be 1(YES) to have a 1(YES) output.
Y = A + B

## Slide 12: NAND
A | B | Y (Output)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
RESULT IS OPPOSITE OF AND
Y = A  B